Notes STM32 Getting Receiver Signals from Joop Brokkings video
We will use the input capture mode in the STM32 chip. How does this mode work
- CNT counts from 0 to the value of the ARR register
- When this value is reached, the timer resets
- The pulse for this counter is determined by the prescaler PCS register
- The input from the receiver is connected to TIM1_CH1 for example
- When the input changes from low to high, this is detected by the CCMR2 and CCER registers and the counter value is stored in the CCR1 register
  - This only captures the rising edge of the signal
  - To capture the falling edge, we will have to reset the register value using the interrupt handling routing
- This generates an interrupt through the DIER register, which can be handled by our interrupt handler

Example using Timer 2 register. Every register holds 4 bytes. So for example: TIMx_CR1 for Timer 2 has an address 0x4000 0000 and TIMx_CR2 has an address of 0x4000 0004